## Slide 2: Overview
Part1 - Introduction
    Design Topics
      Design hierarchy
    Design Procedure
      The major design steps: specification, formulation, optimization, technology mapping, and verification
    Technology Mapping
      From AND, OR, and NOT to other gate types
  Decoders
Part 2
  Encoders
  Multiplexers
  Binary Adders

## Slide 3: Combinational Circuits
A combinational logic circuit has:
  A set of m Boolean inputs,
  A set of n Boolean outputs, and
  n switching functions, each mapping the 2m input combinations to an output such that the current output depends only on the current input values
A block diagram:
m Boolean Inputs
n Boolean Outputs
Combinatorial
Logic
Circuit

## Slide 4: Hierarchical Design
To control the complexity of the function mapping inputs to outputs:
  Decompose the function into smaller pieces called blocks
  Decompose each block’s function into smaller blocks, repeating as necessary until all blocks are small enough
  Any block not decomposed is called a primitive block
  The collection of all blocks including the decomposed ones is a hierarchy
Example: 9-input parity tree (see next slide)
  Top Level: 9 inputs, one output
  2nd Level: Four 3-bit odd parity trees in two levels
  3rd Level: Two 2-bit exclusive-OR functions
  Primitives: Four 2-input NAND gates
  Design requires 4 X 2 X 4 = 32 2-input NAND gates

## Slide 5: Hierarchy for Parity Tree Example
B
O
X
0
X
1
X
2
X
3
X
4
X
5
X
6
X
7
X
8
Z
O
9-Input
odd
function
(a) Symbol for circuit
3-Input
odd
function
A
0
A
1
A
2
B
O
3-Input
odd
function
A
0
A
1
A
2
B
O
3-Input
odd
function
A
0
A
1
A
2
B
O
3-Input
odd
function
A
0
A
1
A
2
X
0
X
1
X
2
X
3
X
4
X
5
X
6
X
7
X
8
Z
O
(b) Circuit as interconnected 3-input odd
function blocks
B
O
A
0
A
1
A
2
(c) 3-input odd function circuit as
interconnected exclusive-OR
blocks
(d) Exclusive-OR block as interconnected
NANDs

## Slide 6: Design Example
Specification
  BCD to Excess-3 code converter
  Transforms BCD code for the decimal digits to Excess-3 code for the decimal digits
  BCD code words for digits 0 through 9: 4-bit patterns 0000 to 1001, respectively
  Excess-3 code words for digits 0 through 9: 4-bit patterns consisting of 3 (binary 0011) added to each BCD code word
  Implementation:
    multiple-level circuit
    NAND gates (including inverters)

## Slide 7: Design Example (continued)
Formulation
  Conversion of 4-bit codes can be most easily formulated by a truth table
  Variables - BCD: A,B,C,D
  Variables - Excess-3 W,X,Y,Z
  Don’t Cares - BCD 1010 to 1111

## Slide 8: Design Example (continued)
Optimization
  2-level using K-maps
W = A + BC + BD
X = C + D + B
Y = CD +
Z =
B
C
D
A
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
1
1
1
1
X
X
X
X
X
X
1
B
C
D
A
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
1
1
1
1
X
X
X
X
X
X
1
B
C
D
A
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
1
1
1
1
X
X
X
X
X
X
1
B
C
D
A
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
1
1
1
X
X
X
X
X
X
1
1
w
z
y
x
B
C
D
B
C
D
D

## Slide 9: Design Example (continued)
Optimization (continued)
  Multiple-level using transformations W = A + BC + BD X = C + D + B Y = CD + Z = G = 7 + 10 + 6 + 0 = 23
  Perform extraction, finding factor:
  T1 = C + D W = A + BT1 X = T1 + B Y = CD + Z = G = 2 + 1 + 4 + 7 + 6 + 0 = 19
B
C
D
B
C
D
D
B
C
D
C
D
D

## Slide 10: Design Example (continued)
Optimization (continued)
  Multiple-level using transformations T1 = C + D W = A + BT1 X = T1 + B Y = CD + Z = G = 19
  An additional extraction not shown in the text since it uses a Boolean transformation: ( = C + D = ):
  W = A + BT1 X = T1 + B Y = CD + Z = G = 2 +1 + 4 + 6 + 4 + 0 = 16!
B
C
D
C
D
D
B
T1
D
T1
C
D
T1

## Slide 11: Design Example (continued)
Technology Mapping
  Mapping with a library containing inverters and 2-input NAND, 2-input NOR, and 2-2 AOI gates
A
B
C
D
W
X
Y
Z

## Slide 12: Decoding
Decoding - the conversion of an n-bit input code to an m-bit output code with n £ m £ 2n such that each valid code word produces a unique output code
Circuits that perform decoding are called decoders
Here, functional blocks for decoding are
  called n-to-m line decoders, where m £ 2n, and
  generate 2n (or fewer) minterms for the n input variables

## Slide 13: Decoder Examples
1-to-2-Line Decoder
2-to-4-Line Decoder
Note that the 2-4-line made up of 2 1-to-2- line decoders and 4 AND gates.

## Slide 14: Decoder with Enable
In general, attach m-enabling circuits to the outputs
See truth table below for function
  Note use of X’s to denote both 0 and 1
  Combination containing two X’s represent four binary combinations
Alternatively, can be viewed as distributing value of signal EN to 1 of 4 outputs
In this case, called a demultiplexer

## Slide 15: 2-to-4 Decoder Diagram

## Slide 16: NAND Only

## Slide 17: Decoder Expansion
General procedure given in book for any decoder with n inputs and 2n outputs.
This procedure builds a decoder backward from the outputs.
The output AND gates are driven by two decoders with their numbers of inputs either equal or differing by 1.
These decoders are then designed using the same procedure until 2-to-1-line decoders are reached.
The procedure can be modified to apply to decoders with the number of outputs ≠ 2n

## Slide 18: 3-to-8-line decoder (without enable)
Consider a 3-to-8-line decoder (without enabler)
A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 |  |  |  |  |  |  | 
0 | 0 | 1 |  | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  | 1 |  |  |  |  | 
0 | 1 | 1 |  |  |  | 1 |  |  |  | 
1 | 0 | 0 |  |  |  |  | 1 |  |  | 
1 | 0 | 1 |  |  |  |  |  | 1 |  | 
1 | 1 | 0 |  |  |  |  |  |  | 1 | 
1 | 1 | 1 |  |  |  |  |  |  |  | 1

## Slide 19: 3-to-8-line Decoder Implementation

## Slide 20: Easier way by Expansion
Decoder expansion
  Combine two or more small decoders with enable inputs to form a larger decoder
3-to-8-line decoder constructed from two 2-to-4-line decoders
    The MSB is connected to the enable inputs
    if A2=0, upper is enabled; if A2=1, lower is enabled.

## Slide 21: Expansion

## Slide 22: Combinational Circuit Design with Decoders
Combinational circuit implementation with decoders
  A decoder provide 2n minterms of n input variables
  Since any Boolean function can be expressed as a sum of minterms, one can use a decoder and external OR gates to implement any combinational function.

## Slide 23: Combinational Circuit Design with Decoders
Realize F (X,Y,Z) = Σ (1, 4, 7) with a decoder:

## Slide 24: Decoder Implementation of a Full Adder
Truth Table: We have two outputs, called S, which stands for sum, and C, which stands for carry. Both sum and carry are functions of X, Y, and Z.

## Slide 25: Decoder Implementation of a Full Adder
The output functions S & C can be expressed in sum-of-minterms forms as follows:
S is implemented by taking minterms 1, 2, 4, and 7 and the OR gates forms the logical sum of minterm for S
Similarly, carry C is implemented by taking logical sum of minterms 3, 5, 6, and 7 from the same decoder