## Slide 2: The Design Procedure
Part 2
  Specification
  Formulation - Obtain a state diagram or state table
  State Assignment - Assign binary codes to the states
Part 3
  Flip-Flop Input Equation Determination - Select flip-flop types and derive flip-flop equations from next state entries in the table
  Output Equation Determination - Derive output equations from output entries in the table
  Technology Mapping - Find circuit from equations and map to flip-flops and gate technology

## Slide 3: Specification
Component Forms of Specification
  Written description
  Mathematical description
  Hardware description language*
  Tabular description*
  Equation description*
  Diagram describing operation (not just structure)*
Relation to Formulation
  If a specification is rigorous at the binary level (marked with * above), then all or part of formulation may be completed

## Slide 4: Formulation: Finding a State Diagram
A state is an abstraction of the history of the past applied inputs to the circuit (including power-up reset or system reset).
  The interpretation of “past inputs” is tied to the synchronous operation of the circuit. E. g., an input value (other than an asynchronous reset) is measured only during the setup-hold time interval for an edge-triggered flip-flop.
Examples:
  State A represents the fact that a 1 input has occurred among the past inputs.
  State B represents the fact that a 0 followed by a 1 have occurred as the most recent past two inputs.

## Slide 5: Formulation: Finding a State Diagram
In specifying a circuit, we use states to remember meaningful properties of past input sequences that are essential to predicting future output values.
A sequence recognizer is a sequential circuit that produces a distinct output value whenever a prescribed pattern of input symbols occur in sequence, i.e, recognizes an input sequence occurence.
We will develop a procedure specific to sequence recognizers to convert a problem statement into a state diagram.
Next, the state diagram, will be converted to a state table from which the circuit will be designed.

## Slide 6: Sequence Recognizer Procedure
To develop a sequence recognizer state diagram:
  Begin in an initial state in which NONE of the initial portion of the sequence has occurred (typically “reset” state).
  Add a state that recognizes that the first symbol has occurred.
  Add states that recognize each successive symbol occurring.
  The final state represents the input sequence (possibly less the final input value) occurence.
  Add state transition arcs which specify what happens when a symbol not in the proper sequence has occurred.
  Add other arcs on non-sequence inputs which transition to states that represent the input subsequence that has occurred.
The last step is required because the circuit must recognize the input sequence regardless of where it occurs within the overall sequence applied since “reset.”.

## Slide 7: State Assignment
Each of the m states must be assigned a unique code
Minimum number of bits required is n such that n ≥ log2 m where x is the smallest integer ≥ x
There are useful state assignments that use more than the minimum number of bits
There are 2n - m unused states

## Slide 8: Sequence Recognizer Example
Example: Recognize the sequence 1101
  Note that the sequence 1111101 contains 1101 and "11" is a proper sub-sequence of the sequence.
Thus, the sequential machine must remember that the first two one's have occurred as it receives another symbol.
Also, the sequence 1101101 contains 1101 as both an initial subsequence and a final subsequence with some overlap, i. e., 1101101 or 1101101.
And, the 1 in the middle, 1101101, is in both subsequences.
The sequence 1101 must be recognized each time it occurs in the input sequence.

## Slide 9: Example: Recognize 1101
Define states for the sequence to be recognized:
  assuming it starts with first symbol,
  continues through each symbol in the sequence to be recognized, and
  uses output 1 to mean the full sequence has occurred,
  with output 0 otherwise.
Starting in the initial state (Arbitrarily named "A"):
  Add a state that recognizes the first "1."
  State "A" is the initial state, and state "B" is the state which represents the fact that the "first" one in the input subsequence has occurred. The output symbol "0" means that the full recognized sequence has not yet occurred.
A
B
1/0

## Slide 10: Example: Recognize 1101 (continued)
After one more 1, we have:
  C is the state obtained when the input sequence has two "1"s.
Finally, after 110 and a 1, we have:
  Transition arcs are used to denote the output function (Mealy Model)
  Output 1 on the arc from D means the sequence has been recognized
  To what state should the arc from state D go? Remember: 1101101 ?
  Note that D is the last state but the output 1 occurs for the input applied in D. This is the case when a Mealy model is assumed.
A
B
1/0
A
B
1/0
C
1/0
0/0
C
1/0
D
1/1

## Slide 11: Example: Recognize 1101 (continued)
Clearly the final 1 in the recognized sequence 1101 is a sub-sequence of 1101. It follows a 0 which is not a sub-sequence of 1101. Thus it should represent the same state reached from the initial state after a first 1 is observed. We obtain:
A
B
1/0
C
1/0
0/0
1/1
D
A
B
1/0
C
1/0
0/0
D
1/1

## Slide 12: Example: Recognize 1101 (continued)
The state have the following abstract meanings:
  A: No proper sub-sequence of the sequence has occurred.
  B: The sub-sequence 1 has occurred.
  C: The sub-sequence 11 has occurred.
  D: The sub-sequence 110 has occurred.
  The 1/1 on the arc from D to B means that the last 1 has occurred and thus, the sequence is recognized.
1/1
A
B
1/0
C
1/0
D
0/0

## Slide 13: Example: Recognize 1101 (continued)
The other arcs are added to each state for inputs not yet listed. Which arcs are missing?
Answer:
"0" arc from A "0" arc from B "1" arc from C "0" arc from D.
1/1
A
B
1/0
C
1/0
D
0/0

## Slide 14: Example: Recognize 1101 (continued)
State transition arcs must represent the fact that an input subsequence has occurred. Thus we get:
Note that the 1 arc from state C to state C implies that State C means two or more 1's have occurred.
C
1/1
A
B
1/0
1/0
D
0/0
0/0
0/0
1/0
0/0

## Slide 15: Formulation: Find State Table
From the State Diagram, we can fill in the State Table.
There are 4 states, one input, and one output. We will choose the form with four rows, one for each current state.
From State A, the 0 and 1 input transitions have been filled in along with the outputs.
1/0
0/0
0/0
1/1
A
B
1/0
C
1/0
D
0/0
0/0
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
B
C
D
1/0
B
0
0/0
A
0

## Slide 16: Formulation: Find State Table
State
Present
From the state diagram, we complete the state table.
What would the state diagram and state table look like for the Moore model?
1/0
0/0
0/0
0/0
1/1
A
B
1/0
C
1/0
D
0/0
Next State
x=0 x=1
Output
x=0 x=1
A
A B
0 0
B
A C
0 0
C
D C
0 0
D
A B
0 1

## Slide 17: State Assignment – Example 1
How may assignments of codes with a minimum number of bits?
  Two – A = 0, B = 1 or A = 1, B = 0
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
A
B
0
0
B
A
B
0
1

## Slide 18: State Assignment – Example 2
Present
State
Next State
x=0 x=1
Output
x=0 x=1
A
A B
0 0
B
A C
0 0
C
D C
0 0
D
A B
0 1

## Slide 19: State Assignment – Example 2 (continued)
Assignment 1: A = 0 0, B = 0 1, C = 1 0, D = 1 1
The resulting coded state table:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 1 1 | 1 0 | 0 | 0
1 1 | 0 0 | 0 1 | 0 | 1

## Slide 20: State Assignment – Example 2 (continued)
Assignment 2: A = 0 0, B = 0 1, C = 1 1, D = 1 0
The resulting coded state table:
Present State | Next State x = 0 x = 1 |  | Output x = 0 x = 1 | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 1 | 0 | 0
1 1 | 1 0 | 1 1 | 0 | 0
1 0 | 0 0 | 0 1 | 0 | 1