## Slide 1: CSE 226: Digital Logic Design Lab Sequence recognizers United International University

## Slide 2: Objective
Implementing Sequence Recognizer using
  J-K Flip flops
  D Flip flops
Our example will detect the bit pattern 1001, while overlap will be supported

## Slide 3: State Diagram
11
1
0
0
1
00
01
10
0
1
1
0

## Slide 4: State table
Present state |  | Input | Next state |  | Output | J1 | K1 | J0 | K0
Q1 | Q0 | x | Q1 | Q0 | z |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | X | 0 | X
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | X
0 | 1 | 0 | 1 | 0 | 0 | 1 | X | X | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | X | X | 0
1 | 0 | 0 | 1 | 1 | 0 | X | 0 | 1 | X
1 | 0 | 1 | 0 | 1 | 0 | X | 1 | 1 | X
1 | 1 | 0 | 0 | 0 | 0 | X | 1 | X | 1
1 | 1 | 1 | 0 | 1 | 1 | X | 1 | X | 0

## Slide 5: Implementing with J-K
Equations and logic diagram

## Slide 6: Implementing Logisim
First, implement the circuit diagram in Logisim.

## Slide 7: 7476: Dual J-K Flip-Flops (with Preset and Clear)

## Slide 8: Timing diagram
Here is one example timing diagram for our sequence detector.
  The flip-flops Q1Q0 start in the initial state, 00.
  On the first three positive clock edges, X is 1, 0, and 0. These inputs cause Q1Q0 to change, so after the third edge Q1Q0 = 11.
  Then when X=1, Z becomes 1 also, meaning that 1001 was found.
The output Z does not have to change at positive clock edges. Instead, it may change whenever X changes, since Z = Q1Q0X.
CLK
Q1
Q0
X
Z
1 2 3 4

## Slide 9: Writing Report
State diagram
Flip-flop assignment table
K-maps
Circuit diagram
Pin diagram of flip-flop IC