## Slide 1: Multiplication of Signed Numbers
CSE 430 – Assignment 4

## Slide 2: Problem Statement
For this assignment you will need to implement the control logic for multiplication of signed numbers using sequence register and decoder method. We will be using 5 bit sign-magnitude form for this. Meaning 1 bit sign and 4 bit magnitude.
In this slide we will be going step by step of what we need to do to implement this control logic

## Slide 3: Step 1: ALU Sub-circuit
First we need design the sub-circuit of our basic ALU. Use your previously designed ALU here.

## Slide 4: Step 2: Accumulator Sub-circuit
We don’t need our accumulator to implement many functions here. We just need it to load the output from ALU or hold it’s current value. For this we will be using a universal shift register (74194).
The shift register operates as follows-
S1S0 = 00  Hold value
S1S0 = 10  Shift right (MSB in SL)
S1S0 = 11  Parallel Load
MR = 0  Reset
Similar to the ALU we check if it can load and value as expected.
Once you have checked that, connect the ALU’s output to the accumulators input, and the accumulators output to the A input of ALU. Now check the components together.

## Slide 5: Step 3: Implement Multiplier register Q
It will be the same as the accumulator. Except we will need provision to load an initial value

## Slide 6: Step 4: Implement Counter
We will need to control the number of iterations depending on the number of bits, 4 in this case. In this case we will not count down from 4 to 0 like the algorithm suggests. It will be easier for us to count up from 0 to 4 and terminate after 4 count.
Use a 74193 to implement the counter

## Slide 7: Step 5: Implement Transition logic
Implement the state transition logic using JK flip flops and a decoder.

## Slide 8: Step 6: Implement the control signals
Implement the control signals as the functions of the states.
Check the values with logicprobes when you are done.

## Slide 9: Control signals of A:
Functions:
S1 = Q1T2 + T3
S0 = Q1T2
RES =
Also, MSB = E
State | S1 | S0 | RES
T1 | 0 | 0 | 0
Q1T2 | 1 | 1 | 1
T3 | 1 | 0 | 1

## Slide 10: Control signals of Q:
Functions:
S1 = T1 + T3
S0 = T1
Also, RES = 1
and MSB = A1
State | S1 | S0
T1 | 1 | 1
T3 | 1 | 0

## Slide 11: Control signals of Counter:
Functions:
D3 – D0 = 0100 (4)
DN = T2.CLK
PL =
MR = 0
Output:
Pz = TCD’

## Slide 12: Step 7: Implement As and E
Use E (like previous assignment)
Implement As = Bs xor Qs

## Slide 13: Control signals of E:
Functions:
JE = Q1T2Cout
KE = T1 + T3 + Q1T2Cout’
State | JE | KE
T1 | 0 | 1
Q1T2 | Cout | Cout’
T3 | 0 | 1

## Slide 14: Final Step:
You are good to go now, check the design for all possible scenarios in

## Slide 15: Deadline
Section B: 02/09
Submit your Proteus files in ELMS.